EXHIBIT 1

STATE OF MARYLAND

TO THE USE OF THE

DEPARTMENT OF BUDGET AND MANAGEMENT

AND

doing business as

Specifications for Leasing of Communications Tower Space

Hagerstown, Washington County, Maryland

# WATER TANK

State’s Point of Contact (Area Manager):

Maryland Department of Public Safety and Correctional Services

Chief Information Officer, Information Technology and Communications Division

Notice Address:

Maryland Department of Public Safety and Correctional Services

Information Technology and Communications Division

6776 Reisterstown Road

Suite 209

Baltimore, MD 21215

Payment Address:

Maryland Department of Public Safety and Correctional Services

Information Technology and Communications Division

6776 Reisterstown Road

Suite 209

Baltimore, MD 21215

Antenna Support Structure:

The existing structure is a State-owned 100 foot, 500,000-gallon water tank.  A structural analysis has been completed for the installation of cellular antennas on the tank catwalk at 78’, with transmission lines being routed down a leg of the tank to the communications building.

Auxiliary Equipment Buildings:

There is an existing environmental monitoring station in the area of the water tank, however, there are no other structures on site.

Antenna Configuration:

Antenna configuration is identified in Table 1.

TABLE 1

| Location | Height | Azimuth | Model | Frequency | Feed line |
| --- | --- | --- | --- | --- | --- |
| A | 78’ | 125 | AP16-850 | 800 | 1 5/8” |
| B | 78’ | 125 | AP-16-850 | 800 | 1 5/8” |
| C | 78’ | 240 | AP16-850 | 800 | 1 5/8” |
| D | 78’ | 240 | AP16-850 | 800 | 1 5/8” |
| E | 78’ | 360 | AP16-850 | 800 | 1 5/8” |
| F | 78’ | 360 | AP16-850 | 800 | 1 5/8” |

Site Security and Fencing:

The site is not currently fenced.  In the event the Correctional Facility requests fencing U. S. Cellular agrees to fence the 12’ X 20’ equipment shelter and the associated tank leg to secure the tank from the possibility of unauthorized access.

Site Access:

The communications site is located on the Hagerstown Correctional Institution property.  There is a gravel access road connecting the water tank to Roxbury Road.  The road will be extended and maintained by ____________ approximately 90’ to allow access to the new equipment shelter.  Access procedures to the site will be governed by the correctional institution’s policies.

Utilities:

A right-of-way to install independent electrical and telephone service will be granted by the State.   The utility easement will also accommodate any future carriers.

Emergency Power:

No emergency power is located at the site.

Removal of Existing Tower:

N/A

Other Considerations:

____________agrees to reserve one standard equipment footprint for installation of radio communications equipment within the shelter for the use of the Maryland Department of Public Safety and Correctional Services or to provide/install and maintain an additional equipment shelter to provide this space for the use of Maryland Department of Public Safety and Correctional Services when requested.

_______________, Inc., doing business as _____________, Proposed Equipment:

Antennas.

Six (6) Panel antennas are approved.  Antennas are to be Scala Model AP16-850.  Centerline of antennas is to be 78’ AGL.  Appurtances shall not protrude below 70’ AGL or above 85’ AGL.  A temporary microwave, 6 GHz panel antenna will be temporarily utilized until telephone service is established.  The panel antenna will be removed within 30 days of the establishment of telephone service.  Any damage to the painted surfaces of the water tank caused by the temporary antenna will be repaired to the satisfaction of the State.

Equipment Shelter and Equipment

One 12’ X 20’ concrete aggregate finish communications equipment shelter to house CDMA cellular equipment will be located adjacent to the water tank. The communications shelter will be set on a poured concrete pad (approximately 10’from the tank). All cellular equipment is to be located within the building exclusive of utilities.  ____________ agrees to reserve one standard equipment footprint for installation of radio communications equipment within the shelter for the use of the Maryland Department of Public Safety and Correctional Services or to provide an additional equipment shelter for the use of Maryland Department of Public Safety and Correctional Services as requested.

Associated cabling to attach antennas to base station equipment.

Six (6) 1 5/8” Andrews LDF7 transmission lines will be connected to the CDMA antennas, routed down a tank leg supported by wave-guide hanger mounts and an ice bridge to the equipment shelter.

Associated Power and Telco junction boxes.

Power and Telco equipment is to be located immediately adjacent to the water tank utilities and routed underground to the 12’ x 20’ communications building.  The power frame contain a six (6) gang box, and the Telco service will be a CSC cabinet, to accommodate all future carriers.

Chain Link Fencing to secure communications equipment.

None